## Slide 1: Beyond Bouncing Boxes
  Fast, yet still Realistic, Deformation and Fracture
Jeff Lander
Darwin 3D, LLC
Luxoflux
James O'Brien
U. of California, Berkeley

## Slide 2: Practical Aspects Using a soft body simulator
How do we implement the techniques discussed in a real-world application?
Aspects important to production
  Pathway for content creation
  Robust!!! as well as consistent
  Integrates with existing architecture
  Low performance impact
  Renders nice models

## Slide 3: Content Creation
Artist don't want to build things out of volume elements
  Need an automated process that works from surface model
  Dynamic model can be a simplified object
  Also need to maintain relationship between artistic and dynamic model
  Custom tweaking will be needed

## Slide 4: Content Creation
Boundary constrained Delaunay tetrahedralization
  Several resources for this. [Shewchuk] has the most readable info.
  Creates a set of tetrahedra from a boundary surface.
  Try to use existing vertices as nodes
  Will create extra nodes as needed
  Good to have settings to adjust min/max volume to refine mesh
  Integrated with toolset for testing/revisions/tweaks

## Slide 5: Input mesh and Tetrahedra

## Slide 6: Simplified Dynamic Model
Can use 1 to 1 mapping with display vertices
Or Use a lower detail dynamic model for the deformation.
Dynamic Mesh deforms hires mesh
  Use matrix blending technique like for skinned characters
  Other methods like FFD would work as well
This complicates things if you want to use any form of fracture

## Slide 7: Stay Tweakable
No good just having a post process that creates the mesh.
You WILL need to change the dynamic model as well as the artistic one.
Keep an associated dynamic mesh file or as data attached to the art mesh.
Need to be able to load, tweak, save...
Make it part of the toolset.

## Slide 8: Robust Dynamic Model
Robustness is key
  Sacrifice realism for stability
Validate stability for your given sim situations.
  Make sure it can't blow up given what you may throw at it.
Arsenal of numerical integrators
  Explicit Euler will not cut it (many papers)
  I currently use a 2nd Order PC and RK-2/4
  Will be adding Implicit Euler for when the going gets real stiff – [See Wu]

## Slide 9: Integration with System
Dynamics need to integrate with existing game elements
In many cases not everything will be made deformable
Deformable material should be able to be anchored to static elements or rigid dynamic pieces.
  Done by supporting pin and spring constraints to material

## Slide 10: Integration Example The trampoline
Dynamics elements pinned to rigid object

## Slide 11: Breaking Links
What if we want to allow break to break?
  Need a method of measuring the stress on each element. Consider a spring:

## Slide 12: Measuring Strain
Engineering Strain
  EE = (l-L)/L
Green Strain
  EG = (l2 – L2)/2L2

## Slide 13: Breaking Links
Determine where a link has broken
  Need to relate the strain to the material properties of the element
  Stress is the value of force per unit area
  Stress is related to strain by the material
    Stress = K EG
    K is measure of stiffness (Young Modulus)
    Hooke's Law of Elastic Materials
  Give this we can set a stress fracture threshold

## Slide 14: Breaking Elements
Extending the same idea to tetrahedra
  Simplified version of O'Brien fracture
  We have a measure of strain on each node
  If it exceeds a threshold, a break has occurred
  Dynamically create a new node and split any attached nodes to respective elements along separation plane.
    Drawback is fractures follow mesh topology

## Slide 15: Breaking Elements Example
Forces produce fracture at element with high stress
These thresholds can easily be set for each material

## Slide 16: Lighting Deformable Model
Recomputing the surface normals for deformable body is expensive
  Object behaves mostly like rigid body
  We can extract a reference frame from the moved model
  This gives a general basis for rotating the surface normals
    Will not be correct in areas of deformation
    In areas where elements at the surface are deformed, normals can be manual recomputed
  See demonstration

## Slide 17: Collision Detection
We know what elements and faces are at the surface
  Track these and use for interaction calculation
AABB Trees sized to the model
  Positions can be quickly indexed to a position in the tree.
  A test point generates a group of elements to test against.
  Distance tests to elements in tree determine potential collisions.

## Slide 18: Collision Detection
Once position of collision is determined
  Force response needs to be applied to nodes of element.
  Barycentric Coordinates provide method for applying the response force

## Slide 19: Performance Issues
Volume elements methods are well suited to modern game hardware
  Mathematics involves much vector processing that can be run in parallel
  Lots of opportunities for task splitting and optimization tricks (dynamic LOD)
  Large portions of many deformable objects can be treated like a rigid body
  Fits well in an overall dynamic system.

## Slide 20: Examples
Basic Deformable Model
Material Properties
Integration with static elements
Breaking Elements
Dynamic Surface Normal calculations
Questions?

## Slide 21: For Further Info
Tetrahedral mesh generation
  Jonathan Shewchuk www-2.cs.cmu.edu/~jrs/
  www.andrew.cmu.edu/user/sowen/softsurv.html
Cel Damage Physics, Penalty Methods, Implicit Euler
  David Wu www.pseudointeractive.com/about.shtml
Collision Detection and Deformable Models
  Cotin, et al, “Real-time elastic deformations of soft tissues for surgery simulation”,1999
  Gino van den Bergen's work www.win.tue.nl/~gino/solid/
James O'Brien Homepage with all of his papers
  www.cs.berkeley.edu/~job/
More references and samples at www.darwin3d.com